MS8-Xany

More than a simple 8-output MultiSwitch decoder for OpenAVRc

MS8-Xany MultiSwitch user manual

Copyright OpenAVRc 2018

# THIS DOCUMENT

## Versions
The version of this document is the last of the version column of the following table.
Version	Date	Reason for update
0.1	20/12/2018	Creation
0.2	01/06/2020	Tulip holder for ATtiny84, diode serigraphy correction
0.3	29/03/2021	- Picture of PCB added / - Correction of jumper ↓ and = position for P1 / - Pinning added for USB/Serial type « FTDI » for P9 / - Minor correction in command table / - ATtiny84 programming with the help of an arduino UNO configured as ArduinoISP added
0.4	27/07/2021	« Pulse » mode commands added (Release MS8 V0.5)

## Copyright
This document is Copyright © 2018-2021 OpenAVRc.
## Disclaimer
The OpenAVRc team is not responsible for any damage that may result from the misuse or possible malfunction of the OpenAVRc transmitter, the MS8-Xany decoder module and/or associated software.
It is therefore up to the end user to estimate, assume the risks and comply with the legislation in force depending on the country of use.
## Contents
This document describes the making of the MS8-Xany decoder module as well as the settings for its use with the OpenAVRc transmitter.
MS8-Xany is a MultiSwitch decoder module with 8 digital outputs.
In addition to the classic MultiSwitch function, MS8-Xany can be set up so that its outputs drive standard servos with digital commands (0/1).
Finally, MS8-Xany can provide an auxiliary proportional channel for driving a standard proportional servo or an ESC.
It is also possible to command each output in « Pulse » mode.
# PRESENTATION OF MS8-XANY
## Overview

X-Any option :
 8 Contacts
(switches)

RX

TX

MS8-Xany

S0
S8
S1
RC

## MS8-Xany decoder specifications
Specification	Value / Feature	Notes
Power supply	+3.3V to +6.6V	Set the "receiver voltage" jumper to "=" or "↓" according to the value of the voltage supplied by the receiver
X-Any Protocol	-Universal digital protocol used by OpenAVRc for remote accessories - Integrity check with 8-bit checksum - Works with all protocols, including 2.4GHz: - PPM Protocol - SPIRfMod Protocols - MultiMod Protocols	Unlike many MultiSwitches, MS8-Xany also works with 2.4GHz HF modules
8 Digital Outputs	- Commanded in Digital mode by transistor output	Outputs configured in "Digital" mode (MultiSwitch)
Output voltage	- Internal: receiver voltage / - External: external voltage 5 to 24V	Selectable by jumper (common to 8 outputs)
Free wheeling diodes	Free wheeling diodes between the 8 outputs and + output power	Selectable by jumper (common to 8 outputs)
8 servo outputs	- Digitally driven / - End positions can be configured / - Duration of movement between end positions is configurable	- Outputs configured in "Servo" mode / - Reversal of servo travel possible by changing extreme values / - Ability to use receiver voltage / - Possibility to use an external voltage (compatible with servos)
1 proportional servo output	Proportional control of a servo from 988μs to 2008μs (0 to 255 steps of 4μs)	Presence of servo control is dynamically detected by MS8-Xany: nothing to configure except at the OpenAVRc transmitter side
Red LED lights when signal is lost	After 1.5 seconds without correct signal	Not managed if proportional servo used (shared connection)
Failsafe	- All outputs go to 0 in case of RC signal loss / - The proportional servo retains its current position	Synchronized with red LED turning on
TTL serial port	USB cable connector / FTDI TTL	For advanced configuration using a "Serial Terminal" application
Dimensions (mm)	L x l x h : 39 x 33 x 12

Page left intentionnally blank

# MS8-XANY SCHEMATIC DIAGRAM

# Making the MS8-XANY DECODER
## Printed circuit board

## Tulip holder for integrated circuits
### Tulip holder for ATtiny84
ATTENTION :
The ATtiny84 shall be programmed before mounting it on the MS8-Xany printed circuit board.
That’s why, it is hghly recommended to mount it on a 14 points tulip holder :

It is also possible to use 2 portions (of 7 points) of a breakable tulip bar :

In both cases, check carefully the orientation of the ATtiny84 before powering the MS8-Xany.
### Tulip holder for ULN2803
In case of bad wiring for the outputs, the ULN2803 may be destroyed.
In order to facilitate its replacement, it is highly recommended to mount it on 18 points tulip holder :

It is also possible to use 2 portions (of 9 points) of a breakable tulip bar :

In both cases, check carefully the orientation of the ULN2803 before powering the MS8-Xany.
## Uploading firmware and configuring fuses
The programming of the microcontroller ATtiny84 is done in 2 phases (in this order):
1. Upload firmware
2. Configure fuses
### Uploading Firmware in ATtiny84
ATTENTION :
The P9 connector (labelled FTDI) is not a programming connector, but is a parametering connector for MS8-Xany (See §Advanced Mode / Servo Control).
2 firmwares are available :
- MS8_Xany_PWM_Vx_y.hex : MS8-Xany is then driven from a PWM output of the receiver
- MS8_Xany_CPPM_Vx_y.hex : MS8-Xany is then driven from the CPPM output of the receiver
The MS8_Xany_PWM_Vx_y.hex PWM version will be more often used.
Using an AVR microcontroller ICSP programmer, upload the MS8_Xany_PWM_Vx_y.hex file to the ATtiny84.
For doing this, we will use an arduino UNO configured as ICSP programmer to load the HEX file in the ATtiny84.
All the programming phase (Firmware loading + Fuses configuration) is preformed before mounting the ATtiny84 on its tulip holder.

### Arduino UNO as ICSP programmer under Windows
Connect your arduino UNO, and with the arduino IDE, load the ArduinoISP sketch by doing :
Files→Examples→11.ArduinoISP
Then, click on Upload : your arduino UNO behaves now as an ICSP programmer.
Do the following wiring to program the ATtiny84 with the arduino UNO :

Copy the Windows sub-directory of the PROG directory on your PC. Open a DOS console (invite command) and go in this Windows directory.
If required, edit the prog_ms8.bat file with a text editor in order to redefine :
1. the right serial port used by the arduino UNO : COMx
2. the HEX file you want to load :
(MS8_Xany_PWM_Vx.y._HEX, or MS8_Xany_CPPM_Vx.y._HEX)
In case, you don’t know which one to choose, take MS8_Xany_PWM_Vx.y._HEX.
In the DOS console, launch the prog_ms8.bat command and follow instructions.
The HEX file will be loaded and the fuses will be automatically programmed.
### Arduino UNO as ICSP programmer under Linux
Connect your arduino UNO, and with the arduino IDE, load the ArduinoISP sketch by doing :
Files→Examples→11.ArduinoISP
Then, click on Upload : your arduino UNO behaves now as an ICSP programmer.
Do the following wiring to program the ATtiny84 with the arduino UNO :

Copy the Linux sub-directory of the PROG directory on your PC. Open a terminal console and go in this Linux directory.
If required, edit the prog_ms8.sh file with a text editor in order to redefine :
1. the right serial port used by the arduino UNO : for example, /dev/ttyACM0
2. the HEX file you want to load :
(MS8_Xany_PWM_Vx.y._HEX, or MS8_Xany_CPPM_Vx.y._HEX)
In case, you don’t know which one to choose, take MS8_Xany_PWM_Vx.y._HEX.
In the terminal console, launch the ./prog_ms8.sh command and follow instructions.
The HEX file will be loaded and the fuses will be automatically programmed.

### Very important note about the value of the fuses

Once the ATtiny84 configured (with its fuses), it is no more possible to directly re-program it with an ICSP programmer since this one needs the Reset function of the ATtiny84.

This is due to the fact the MS8-Xany firmware needs the Reset pin, but configured as an output to drive the « Signal lost » led and to drive the proportional output.

If, for any reason, you need to re-program your ATtiny84, it will be needed to restore the Reset function of the Reset pin.

To do that, it is mandatory to apply calibrated voltage (12V) on the Reset pin. A « Fuse Resetter » box is then needed.

After doing this, the ATtiny84 becomes programmable again using an ICSP programmer.

# Usage
## Connecting to a receiver
Before connecting MS8-Xany to the receiver, it is imperative to measure the voltage supplied by the receiver.
If the available voltage between the - and + pins of the 3-pin connector of the channel used is:
     1. Lower than 5.7V, set the jumper "receiver voltage" to "="
     2. Higher than 5.7V, set the jumper "receiver voltage" to "↓"

S + -

S + -
S0

S1
S2
S3
S4
S5
S6
S7
S8
RC Input (Receiver ouput)

S
+
-

Position « = »
Position « ↓ »

## Standard Mode : MultiSwitch / Digital switch
After uploading the firmware, MultiSwitch is the default mode: the digital switching mode of the 8 S1 to S8 outputs. So there is nothing else to configure to operate in MultiSwitch mode.
### Wiring the loads on the outputs
The MS8-Xany is then used as a standard MultiSwitch module:
- The "loads" (like: a lamp) are connected to the S1 to S8 outputs between the pins "S" and "+", the 8 row points of "-" at the edge of the board is not used in this case.

S + -

S1
S2
S3
S4
S5
S6
S7
S8
Lamp

S
+
-
RC Input (Receiver ouput)

S0

S + -

### Selecting the supply voltage for the S1 to S8 outputs

S
+
-
RC Input (Receiver ouput)

S0

S + -
+ -
5V < VExt < 24V

Position « VRx »
Position « VExt »

S1
S2
S3
S4
S5
S6
S7
S8
S + -
+VRx

It is possible to supply the S1 to S8 outputs (supply to +) from:
+VRx voltage supplied by the receiver (Beware of the current consumption on the outputs!)
        → Power selection jumper on "VRx"
2. An external VExt voltage (5V to 24V) applied to the 2-pin connector at the bottom right
  of the board
 → Power selection jumper on "VExt"
### Free wheeling diodes
If the "loads" connected to the outputs are inductive (eg relays), the internal free wheeling diodes shall be connected, otherwise there is a risk to destroy the ULN2803.
S + -

Diode connected position
Diode disconnected position

S1
S2
S3
S4
S5
S6
S7
S8

S
+
-

RC Input (Receiver ouput)

S0
S + -

### Direct relay control with integrated diodes in the ULN2803

S1
S2
S3
S4
S5
S6
S7
S8

S0

Relay
S
+
-
S + -

RC Input (Receiver ouput)

### Controlling opto-isolated relays
There are very cheap "relay modules" often called "Arduino Relay Module". These modules include an opto-coupler allowing a total isolation between the control voltage and the supply voltage of the coils of the relays.

Yellow Jumper

The equivalent circuit diagram of one relay channel is given below:

- VCC is the opto-coupler control voltage: accessible on the connector on the edge of the board
- JD-VCC is the control voltage of the relay coils: accessible on one of the jumper connector pins

Important Note:
To achieve full isolation between VCC and JD-VCC, the yellow jumper shall be removed.

### Recommended connections for 5V opto-isolated relays

GND
JD-VCC

VCC
(only one needed)
In1
S1
S2
S3
S4
S5
S6
S7
S8
Separate power supply for relay coils:
+ 4.8V to + 7.2V
_
+
+ -

Position « VRx »

*

S0

S
+
-

RC Input
(Receiver output)
S + -

- The optocouplers are powered by the receiver voltage (total consumption: around 10 mA)
- VCC of the relay board is connected to one of the OUTPUT_1X8 supply pins
- In1 of the relay board is connected to the S1 output
- In2 of the relay board is connected to the S2 output, etc.
- Relay coils are powered by a separate power supply (+ 4.8V to + 7.2V)
→ Since the power supplies are completely isolated, the receiver voltage will not be disturbed during relay switching: no risk of losing RC control.
* : On some "relay module" models, there is no GND pin near the JD-VCC. In this case, use the GND pin close to the In1 pin on the other connector.
## X-Any configuration at the OpenAVRc transmitter side
Refer to the OpenAVRc manual to configure the X-Any instance with the following parameters:
1. The channel number shall correspond to the channel number on which the MS8-Xany decoder will be connected to the receiver
2. The number of repetitions will be first set to 3 (as soon as it will work, it will be possible to reduce this value to reach the maximum reactivity allowed by your HF set).
3. Configure "Sw." with Sw.8: this will transmit the state of the 8 contacts
4. If the proportional servo will be used on MS8-Xany, select one of the proposed choices by
  « Prop. », this will add the transmission of the proportionnal value.
## Advanced Mode / Servo Control
The MS8-Xany decoder has an access for advanced configurations: a TTL serial port.
It is this serial access that will allow the use of servos connected to the S1 to S8 outputs.
In this case, the "+" output voltage must be compatible with the servos!
### Using the serial port on MS8-Xany
To access the serial port of MS8-Xany, you need a USB / TTL serial cable eg "FTDI" type.

The necessary pins on the USB cable / TTL series are:
- GND « FTDI »	→ Pin 6 of P9
  S + -
- +5V « FTDI »	→ Not connected
  1
  2
  3
  4
  6
  5
  S
  +
  -

  Battery Pack 4,8V-6V
- TX « FTDI »	→ Pin 3 of P9
- RX « FTDI »	→ Pin 2 of P9

S0
S + -
S1
S2
S3
S4
S5
S6
S7
S8
1. Connect USB side of the USB / TTL serial cable to an USB port on a PC
2. On the PC, open a Serial Terminal, for example, PuTTY, TeraTerm, HyperTerminal, GtkTerm, or CoolTerm with the following parameters: 19200 baud, 8 data bits, 1 stop bit, no parity.
Depending on the Serial Terminal, it may be necessary to enable automatic line feeds on receipt of CR / LF to have a good display.
3. Connect a 4,8V à 6V Battery pack on the MS8-Xany RC connector : this pack will provide the power.
4. Within 3 seconds after connecting the Battery pack, press the "Enter" key on your keyboard, the message "MS8 VX.Y" should appear on the Serial Terminal as shown below. If this is not the case, disconnect the Battery pack and repeat step 3 above.

Example of connection with GtkTerm Terminal on Linux
### MS8-Xany command messages

The list of messages supported by MS8-Xany is given in the following table:
←Command/→Response	Action	Notes
←Enter / →MS8 Vx.y	If sent within the 3 seconds after power on, the decoder enters Terminal mode	If failed and 3 seconds elapsed, unplug and reconnect the 6-pin USB / TTL serial cable connector
←S0? / →S0=Pos:4usStepOffset	Returns the current position in μs and the 4usStepOffset command which is the number of steps of 4μs (value between 0 and 255) to be added to 988 to have the pulse width in μs for the proportional servo	Pulse width (us) = 988 + ( 4usStepOffset x 4)
←S0=Pos / →S0	Sets the position in μs for proportional servo	Returns ERR, if value not between 988 and 2008
←Sx? / →Sx=D;M:C / or / →Sx=S;M;Pos0;Pos1;Dur:C	If x is between 1 and 8, returns the configuration of the output No. x and the state "C" of the associated current Command (0 or 1) / - If the output is configured as MultiSwitch Digital output, the answer is: Sx = D;M:C / D = Digital (Digital) / M=command Mode (N : Normal, P : Pulse) / - If the output is configured as a Servo output, the response is: Sx = S;M;Pos0;Pos1;Dur:C with / S=Servo / M=command Mode (N : Normal, P : Pulse) / Pos0 = the position in μs for the state 0, Pos1 = the position in μs for the state 1, and Dur = the duration (in ms) of the movement of the servo between Pos0 and Pos1	Returns ERR, if / - Value x not between 0 and 8 / - Pos0 or Pos1 < 600 / - Pos0 or Pos1 > 2400 / Sample answers: / S1=D;N:0 / S2=D;P:1 / S3=S;N;1000;2000;5000:0 / S4=S;P;2300;600;8500:1
←Sx=D;M / →Sx	Sets the output x to be Digital / M=command Mode (N : Normal, P : Pulse)	S1=D;N / S2=D;P
←Sx=S;Pos0;Pos1;Dur / →Sx	Sets the output x as servo with Pos0 μs for 0, Pos1 μs for 1, and Dur ms	The real value in ms is internally recalculated by MS8-Xany taking into account the different resolutions / limitations and may be different when displayed.
←Sx=C / →Sx	If x is between 1 and 8, "C" defines the State (0 or 1) for the output x, whether the type is either Digital or Servo	Very handy for testing using the serial access without RC.
←C? / →C=Ch	Returns the channel used in CPPM mode	Command only available with the firmware in CPPM mode
←C=Ch / →C	Set the used channel in CPPM mode
←Q	Exit Terminal Mode: MS8-Xany can be connected to receiver	Do not forget to disconnect the USB / TTL cable!

### Real configuration example
In the example below:
     • The pulse width for the servo connected to the proportional S0 output is:
[988 + (242 x 4)] = 1956 μs
→ the command (= the number of 4 μs steps to add to 988 μs) would be 242 for the pulse	width of 1956 μs
     • The outputs S1, S2, S3, S4 and S5 are Digital type (MultiSwitch) type, their states are respectively 0, 1, 0, 0 and 0. Ouput S1 is commanded in Pulse mode.
     • The outputs S6, S7 and S8 are Servo type, their commands are respectively 0, 0 and 1. Ouput S7 is commanded in Pulse mode.

Counterclockwise servo movement
If the contact N°1 at transmitter side is closed (Command=1), the pulse of the servo connected to the output N°1 goes from 600 µs to 2300 µs (→ a movement of around 180°) in 8,5 seconds, and goes from 2300 µs to 600 µs (→ a movement of around 180°) in 8,5 seconds if the contact N°1 at transmitter side is opened (Command=0).

S1
S2
S3
S4
S5
S6
S7
S8

Command=1
Position=2300µs
Command=0
Position=600µs
Duration of
Movement=8,5 s
S2

Position « VRx »

Ex : S1=S;N;0600;2300;8500

S + -

S0

RC Input
(Receiver output)
Clockwise servo movement
S
+
-
With MS8-Xany, it’s possible to obtain a movement in the opposite direction : just swap the extreme positions (Pos0 and Pos1).
If the contact N°2 at transmitter side is closed (Command=1), the pulse of the servo connected to the output N°2 goes from 2000 µs to 1000 µs (→ a movement of around 100°) in 1,67 seconds, and goes from 1000 µs to 2000 µs (→ a movement of around 100°) in 1,67 seconds if the contact N°2 at transmitter side is opened (Command=0).

S1
S2
S3
S4
S5
S6
S7
S8

Command=1
Position=2000µs
Command=0
Position=1000µs
Duration of
Movement=1,67 s
S2

Position « VRx »

Ex : S2=S;N;2000;1000;1666
RC Input
(Receiver output)
S
+
-
S0
S + -

### Normal mode and Pulse mode command
Whatever the output is configured in Digital type (Multiswitch) or in Servo type, it is needed to define the command mode :
- Sx=D;M	(with M equal to N for Normal or P for Pulse)
- Sx=S;M;1000;2000;5000	(with M equal to N for Normal or P for Pulse)
Let’s suppose the following configuration and, at transmitter side, S1 et S2 are commanded with the contacts of push-buttons :
S1=D;N to control a foghorn
S2=D;P to control a light
In both cases, the outputs are Digital type (Multiswitch), but S1 is commanded in Normal mode, wheras S2 is commanded in Pulse mode.

Case of Normal mode :
While the C1 contact is closed, the S1 output is 1 and the foghorn is enabled.
As soon as the C1 contact is released, the S1 output is 0 and the foghorn is disabled.
To summarize, the S1 output follows the status of the C1 contact.

Case of Pulse mode :
While the C1 contact is closed, the S1 output is 1 and the ligth is enabled.
As soon as the C2 contact is released, the S2 output remains to 1 and the light is still enabled.
To disable the light, it is neede to close again the C2 contact.
To summarize, a pulse on the C2 contact enables the S2 output, and a new pulse on the C2 contact disables the S2 output and so on.

Note :
If the type of the output is Servo and the command mode is Pulse, a first pulse on the push-button, trigs the servo motion until the position N°1 and a second pulse trigs the servo motion to the position N°2.
Ex : S3=S;P;1000;2000;5000